## Slide 1: Crawl-Trainer Progress Report Group 9
Tomisin Akinyemi, Katherine Lauer, Lauren Pickman

## Slide 2: Background
Creating a crawling assistive device as an early intervention method for children with gross motor delay.
  8.7% of infants have gross motor delay
  Gross motor delay can be caused by genetic disorders, premature birth, neuromuscular disorders, or developmental disorders

## Slide 3: Overview
Project Changes
Design Alternatives and Analysis
Chosen Solution

## Slide 4: Project Changes

## Slide 5: Updated Design Specifications
Specification | Description
Safety | All materials must be non-toxic and safe for children with no sharp edges or dangerous components. The device must keep children in safe body positions to prevent injury.
Weight Bearing | Must provide trunk support. This must support up to 18 kg, which is the 95th percentile weight of a 3 year old.
Bouncing motion | Must create a slight up-and-down bouncing motion or “springiness” in order to provide sensory stimulation which helps to interrupt ataxic muscle movements.
Contact spatial awareness | Must keep child grounded in space via gravitational awareness, with minimal visual or physical obstruction of their surroundings.
Range of motion | Child must be able to navigate and pivot around in all directions.
Updated
New

## Slide 6: Updated Gantt Chart

## Slide 7: Design Alternatives

## Slide 8: Pugh Chart categories
Highest Weighted
Safety: Materials are non-toxic with no sharp edges. Puts child in a safe body position.
Age: Can be used by ages 1-3
Adjustable: Can be adjusted to accommodate a wide array of heights, to account for growth

## Slide 9: Pugh Chart categories
Highest Weighted (5)
Safety
Age
Adjustable
Other Important Factors (4)
Ease of Use
Weight Bearing/Support
Range of Motion
Contact Spatial Awareness

## Slide 10: Considered Designs
DIY Inspired Solutions
Trunk Support on Wheels
Modified Skateboard
Sensor-Feedback System
Motion Sensor Suit
Robotic
Suspension
Automated Leg Exoskeleton
Multi-Point Bungee System
Foam Roller
Hand-Held Sling
Table Support
Neoprene Sling
Crawl-Trainer
Wall-Mounted Sensors

## Slide 11: DIY Solutions: Foam Roller and Hand-Held Sling
How to Teach Baby to Crawl , Baby Exercises and Activities, 26 May 2015, https://www.youtube.com/watch?v=s0eVO50vddA&feature=youtu.be
Talmud, Rebecca. “Teaching Children to Crawl.” DINOSAUR PHYSICAL THERAPY, 26 July 2016, https://blog.dinopt.com/teaching-children-to-crawl/.
PROS
CONS
Inexpensive
Durable
Portable
Small
Unsafe
Requires proper training/technique for adult
Limited range of motion

## Slide 12: DIY Solutions: Foam Roller and Hand-Held Sling
Neoprene Sling Rank: #7 out of 10
Foam Roller Rank: #10 out of 10
Both have lowest possible safety score

## Slide 13: Sensor-Feedback: Wall-Mounted Sensors
PROS
CONS
Need additional trunk support
Limits range of motion
Concerns with pets or children playing with electrical components
No bouncing motion
Does not take up much space
Works for many ages

## Slide 14: Sensor-Feedback: Motion Sensor Suit
PROS
CONS
Expensive – need multiple suits as child grows
Safety concerns with electrical components so close to child
Need additional trunk support
No bouncing motion
Custom to fit specific child
Portable
Unrestricted motion

## Slide 15: Sensor-Feedback: Pugh Chart
Rank: #8 of 10
#6 of 10

## Slide 16: Robotic: Automated Leg Exoskeleton
PROS
CONS
Proper positioning with trunk support
Custom fit to child
Cost
No bouncing motion sensory input
Passive motion
Proximity of circuitry to child’s body

## Slide 17: Robotic: Pugh Chart
Rank: #9 of 10

## Slide 18: Suspension: Multi-Point Bungee System
“CrawlAhead.” CrawlAhead | LiteGait.com, LiteGait, https://litegait.com/products/CrawlAhead.
Adjustable bungee cords above key weight bearing points: trunk, shoulders, hips
PROS
CONS
Adjustable height
Some bouncing motion for sensory stimulus
Weight bearing
Limits gravitational/spatial awareness -> ”floating” sensation
Multiple straps and harness are difficult to use
Need professional to properly adjust bungee cords

## Slide 19: Suspension: Pugh Chart
Rank: #3 of 10

## Slide 20: Trunk Support on Wheels: Table Support
“Adjustable Crawl Trainer.” Flaghouse, Flaghouse, https://www.flaghouse.com/Positioning-Mobility/Crawling/Adjustable-Crawl-Trainer.axd.
PROS
CONS
Adjustable height
Trunk support
Durable
Spatial awareness
No bouncing motion for sensory input
Bulky
Considered modifying the device below with higher sides and a body strap

## Slide 21: Trunk Support on Wheels: Neoprene Sling
PROS
CONS
Some bouncing motion for sensory stimulus
Range of motion
Spatial awareness
Potential need for multiple slings: need to support correct points on chest and hips
Neoprene

## Slide 22: Trunk Support on Wheels: Modified Skateboard
PROS
CONS
Ease of use
Would work for children 1-3 with minimal adjustments
Range of motion
Does not put child in a proper crawling position
No bouncing motion

## Slide 23: Trunk Support on Wheels: Pugh Chart
#5 of 10
#4 of 10
#2 of 10

## Slide 24: Chosen Solution

## Slide 25: The Crawl-Trainer
Wheels: Allow motion in all directions
Padded foam top: Fits to child’s body and decreases discomfort
Body strap and high sides: Keeps child safely in place with proper positioning
Adjustable bar: Can adjust to correct height for children ages 1-3

## Slide 26: The Crawl-Trainer
Metal bars under tension:
Provide sensory feedback via bouncing motion
Angle of platform reacts to weight distribution
Bouncing/rocking motion:
Calming, sensory feedback
Breaks up ataxic movements to allow for motor planning

## Slide 27: The Crawl-Trainer: Pugh Chart
#1 of 10

## Slide 28: The Crawl-Trainer: Top Performer
The Crawl Trainer
Safety
Easy to use
Bouncing motion
Weight support
Adjustable
Useful for ages 1-3
Range of motion

## Slide 29: Proposed Budget

## Slide 30: Questions?

## Slide 31: Sources
“Adjustable Crawl Trainer.” Flaghouse, Flaghouse, https://www.flaghouse.com/Positioning-Mobility/Crawling/Adjustable-Crawl-Trainer.axd.
“CrawlAhead.” CrawlAhead | LiteGait.com, LiteGait, https://litegait.com/products/CrawlAhead.
How to Teach Baby to Crawl , Baby Exercises and Activities, 26 May 2015, https://www.youtube.com/watch?v=s0eVO50vddA&feature=youtube.
“Cross Crawling.” CogniKids, 28 Nov. 2016, https://cognikids.com/2016/01/28/cross-crawling/.
“Data Table of Infant Height-for-Age Charts.” CDC , National Center for Health Statistics, 23 Aug. 2001, https://www.cdc.gov/growthcharts/html_charts/lenageinf.htm#females.
“Data Table of Infant Weight-for-Age Charts.” CDC , National Center for Health Statistics, 23 Aug. 2001, https://www.cdc.gov/growthcharts/html_charts/wtageinf.htm#females.
Intermountain Healthcare. Gross Motor Delay: Rehabilitation: Pediatrics. n/a n/a 2017. 30 September 2019 <https://intermountainhealthcare.org/services/pediatrics/services/rehabilitation/services/gross-motor-delay/>.
McNamara, Lindsay. Ataxia Overview. 11 Feb. 2019, https://www.hopkinsmedicine.org/neurology_neurosurgery/centers_clinics/ataxia/conditions/.
Perlut PT, Susan. Personal Interview. 19 Nov. 2019.
Talmud, Rebecca. “Teaching Children to Crawl.” DINOSAUR PHYSICAL THERAPY, 26 July 2016, https://blog.dinopt.com/teaching-children-to-crawl/.